iptables is a command line interface used to set up and maintain tables for the Netfilter firewall for IPv4, included in the Linux kernel. The firewall matches packets with rules defined in these tables and then takes the specified action on a possible match.
- Tables is the name for a set of chains.
- Chain is a collection of rules.
- Rule is a condition used to match packets.
- Target is action taken when a possible rule matches. Examples of the target are ACCEPT, DROP, QUEUE.
- Policy is the default action taken in case of no match with the inbuilt chains and can be ACCEPT or DROP.
Syntax:
iptables --table TABLE -A/-C/-D... CHAIN rule --jump Target

TYPES OF IPTABLES :

1. Filter - this is the default iptable or can say, the main table. Its main purpose is to just filter the packets - whether to accept a packet request or to deny it.
2. Nat - Nat stands for network administration. It includes PREROUTING AND POSTROUTING chains.
3. Mangle - this is for specialised packet alteration. It includes PREROUTING AND OUTPUT chains.
4. Raw - Configures exemptions from connection tracking. Built-in chains are PREROUTING and OUTPUT.
5. Security - Used for Mandatory Access Control

CHAINS :

few built-in chains that are included in tables. They are:
- INPUT :set of rules for packets destined to localhost sockets.
- FORWARD :for packets routed through the device.
- OUTPUT :for locally generated packets, meant to be transmitted outside.
- PREROUTING :for modifying packets as they arrive.
- POSTROUTING :for modifying packets as they are leaving.
Note: User-defined chains can also be created.

OPTIONS
A-append	D-delete	I-insert	R-replace	Z-zero counters	L-list
P-policy	F-flush	E-rename	N-new user defined chain	X-delete chain

-A, –append : Append to the chain provided in parameters.
Syntax:
iptables [-t table] --append [chain] [parameters]
Example: This command drops all the traffic coming on any port.
iptables -t filter --append INPUT -j DROP

-D, –delete : Delete rule from the specified chain.
Syntax:
iptables [-t table] --delete [chain] [rule_number]
Example: This command deletes the rule 2 from INPUT chain.
iptables -t filter --delete INPUT 2

-C, –check :Check if a rule is present in the chain or not. It returns 0 if the rule exists and returns 1 if it does not.
Syntax:
iptables [-t table] --check [chain] [parameters]
Example: This command checks whether the specified rule is present in the INPUT chain.
iptables -t filter --check INPUT -s 192.168.1.123 -j DROP
(to get output for the above command, “above command” ; echo $?

-L, --list
Syntax:
sudo iptables -t filter --list

PARAMETERS
The parameters provided with the iptables command is used to match the packet and perform the specified action. The common parameters are:
-p, –proto : is the protocol that the packet follows. Possible values maybe: tcp, udp, icmp, ssh etc.
Syntax:
iptables [-t table] -A [chain] -p {protocol_name} [target]
Example: This command appends a rule in the INPUT chain to drop all udp packets.
iptables -t filter -A INPUT -p udp -j DROP

-s, –source: is used to match with the source address of the packet.
Syntax:
iptables [-t table] -A [chain] -s {source_address} [target]
Example: This command appends a rule in the INPUT chain to accept all packets originating from 192.168.1.230.
iptables -t filter -A INPUT -s 192.168.1.230 -j ACCEPT

-d, –destination : is used to match with the destination address of the packet.	Syntax:
iptables [-t table] -A [chain] -d {destination_address} [target]
Example: This command appends a rule in the OUTPUT chain to drop all packets destined for 192.168.1.123.
iptables -t filter -A OUTPUT -d 192.168.1.123 -j DROP

-i, –in-interface : matches packets with the specified in-interface and takes the action.
Syntax:
iptables [-t table] -A [chain] -i {interface} [target]
Example: This command appends a rule in the INPUT chain to drop all packets destined for wireless interface.
iptables -t filter -A INPUT -i wlan0 -j DROP

1. -o, –out-interface : matches packets with the specified out-interface.
2. -j, –jump : this parameter specifies the action to be taken on a match.
   Syntax:
   iptables [-t table] -A [chain] [parameters] -j {target}
   Example: This command adds a rule in the FORWARD chain to drop all packets.
   iptables -t filter -A FORWARD -j DROP

FEW KEY-NOTES :
Can remove all filtering rules and user created chains.
sudo iptables --flush
- To save the iptables configuration use:
  sudo iptables-save
- Restoring iptables config can be done with:
  sudo iptables-restore

Iptables uses 3 main chains, namely, INPUT, OUTPUT and FORWARD.
Input – This chain is used to control the behavior for incoming connections. For example, if a user attempts to SSH into your PC/server, iptables will attempt to match the IP address and port to a rule in the input chain.
Forward – This chain is used for incoming connections that aren’t actually being delivered locally. Think of a router – data is always being sent to it but rarely actually destined for the router itself; the data is just forwarded to its target. Unless you’re doing some kind of routing, NATing, or something else on your system that requires forwarding, you won’t even use this chain.
Output – This chain is used for outgoing connections. For example, if you try to ping howtogeek.com, iptables will check its output chain to see what the rules are regarding ping and howtogeek.com before making a decision to allow or deny the connection attempt.

To check the current policy configurations, command is:
iptables -L
The three most basic and commonly used “responses” :
1. Accept – Allow the connection.
2. Drop – Drop the connection, act like it never happened. This is best if you don’t want the source to realize your system exists. This basically doesn’t reply to the sender about discarding the messages.
3. Reject – Doesn’t allow the connection, but sends back an error. This is best if you don’t want a particular source to connect to your system, but you want them to know that your firewall blocked them.

BLOCKING CONNECTIONS :
Connections from a single IP address
iptables -A INPUT -s 10.10.10.10 -j DROP
Connections from a range of IP addresses
iptables -A INPUT -s 10.10.10.0/24 -j DROP
Or
iptables -A INPUT -s 10.10.10.0/255.255.255.0 -j DROP
Connections to a specific port
iptables -A INPUT -p tcp --dport ssh -s 10.10.10.10 -j DROP
Block SSH connections from any IP address.
iptables -A INPUT -p tcp --dport ssh -j DROP

TAGS :
-L -> List the currently configured iptables rules:
iptables -L
-n -> list everything numerically - basically hostnames, protocols, and networks	are listed as numbers.
-v -> give you packet and byte information
-F -> flush or clear the configured files
iptables -F

SAVING CHANGES.
COMMAND : sudo /sbin/iptables-save
Shell i/o redirection happens before the shell executes your command...in other words, when you write:
sudo somecommand >> /etc/profile
The >> /etc/profile part is performed as the current user, not as root. That's why you're getting the "permission denied" message.

DIFFERENT WAYS FOR SAVING CHANGES :
Iptables-save

Saving in a file iptables-save > /etc/iptablesRule.v4

Restoring from file iptables-save < /etc/iptablesRule.v4

 BASIC COMMANDS :

With root permissions,
sudo iptables -L -n -v
: to list out the default iptable,
L -> list
N -> numeric format
V -> verbose

UFW
To enable ufw,
sudo ufw enable
{ By default,
this denies connections }

To disable ufw,
sudo ufw disbale

To check all ufw rules in detail,
sudo ufw status verbose

In the rules, initially it would show,
default : deny(incoming) , allow(outgoing) , disabled(routed)

To add a rule,
sudo ufw allow port_num

To allow a specific IP,
sudo ufw allow from “Ip_address” to any port port_num

*extra*
Subnetting -
/8 -> class A
/16 -> class B
/24 -> class AC

To allow an IP range,
sudo ufw allow from ip_address/24 to any port port_num

To allow a protocol,
sudo ufw allow protocol_name

To check for status along a serial number with it,
sudo ufw status numbered

* BLOCKING / REMOVING CONNECTIONS *

To remove a connection,
sudo ufw delete serial_number

To reset connections,
sudo ufw reset
{ upon prompt, press y }

USECASE OF UFW

So, with other protocols like ssh and ftp, open for everyone to connect, results in a massive security loophole. The need for firewall, thus originated. It would allow us remote access to the system but in a limited fashion, like, for example, open to certain ip addresses, etc.

If we do not lock down ssh or ftp or for that matter, any other protocol, we are creating a massive vunerability to our system by letting ssh or other protocol’s designated port open for everyone. With firewall, we provide remote access but also provides security lockdown to avoid malicious users and hackers to gain access.

UFW – stands for Uncomplicated firewall.

Ufw – is a program for managing a netfilter firewall. It aims to provide an easy to use interface for the user.

Options available :
enable, disable, reset, reload, status, logging, default, show, allow, deny, reject, limit, delete, insert, prepend,

LOGGING
       ufw supports multiple logging levels. ufw defaults to a loglevel of 'low' when a loglevel is not specified. Users may specify a loglevel with:
        ufw logging LEVEL
       LEVEL may be 'off', 'low', 'medium', 'high' and 'full'. Log levels are
       defined as:

       1. off - disables ufw managed logging

       2. low - logs all blocked packets not matching the defined policy	(with rate limiting), as well as packets matching logged rules

       3. medium - log level low, plus all allowed packets not matching the	defined policy, all INVALID packets, and all new connections.	All logging is done with rate limiting.

       4. high - log level medium (without rate limiting), plus all packets	with rate limiting
       5. full - log level high without rate limiting

       Loglevels above medium generate a lot of logging output, and may quickly fill up your disk. Loglevel medium may generate a lot of logging output on a busy system.

Back to Iptables :

Chains can be built-in or even user-defined.

Q. Can there be user-defined tables?

Chain – is a list of rules which can match a set of packets.

Rule – a rule specifies what to do with the packet that matches.

Target – an action that would be performed upon matching condition being true.

=> A firewall rule specifies criteria for a packet and a target. If packet doesn’t match, the next rule in the chain would be examined. If it matches, the next rule is specified by the value of the target, can be terminating or non-terminating.

Various OPTIONS available :
-t table
-A append
-C check
-D delete
-I insert
-R replace
-S list-rules
-F flush
-L list
-Z zero ( zeroes the packet and the byte counters of a chain / all chains)
-N new-chain
-X delete-chain
-P poilcy
-E rename
-h help

Various OPTIONS available :
-p –protocol => default = all or numerical zero (0)
-s –source –src
-d –destination –dst
-m –match
-j –jump // processing ends here
-g –goto // processing continues in a user specified chain.
-i –in-interface interface_name
-o –out-interface
-f –fragment
-c –set-counters
-v –verbose
-M –modprobe

iptables-save => dump iptables rules to stdout

iptables-save [-M modprobe] [-c] [-t table] =>

modprobe- specifies path to modprobe program
By default, iptables-save inspects procsys/kernel/modprobe
to determine executable’s path.

-c / --counters – includes current vaues of all packet and byte counters.

Modprobe – adds/removes modules from the Linux kernel

iptables-apply => safer way to update iptables remotely

* default timeoout is 10 seconds. (-t / --timeout )

iptables-restore =>

iptables-restore [-chntv] [-M modprobe] [-T name] [file]

-c counters
-n no-flush (prev data is kept intact)
-h help
-t test
-T table
-v verbose

*Masq*